## Slide 1: Visualization of scoliotic spine using ultrasound-accessible skeletal landmarks
Ben Church1, Andras Lasso1, Christopher Schlenger, Daniel P. Borschneck2, Parvin Mousavi1, Gabor Fichtinger1,2, Tamas Ungi1,2
Surgery, School of Computing, Queen’s University, Kingston, ON, Canada
Department of Surgery, Queen’s University, Kingston, ON, Canada

## Slide 2: Introduction - Scoliosis
Scoliosis is lateral spinal curvature
Curvature progresses with growth
Regular assessment helps ensure early treatment

## Slide 3: Introduction - Assessment
Gold-standard assessment method is X-ray imaging
Cobb angle is measured
Quantifies severity of scoliosis

## Slide 4: Introduction – Tracked Ultrasound
Motivated by X-ray health risks
Ungi et al. [1] investigated sagittal snapshots
Cheung et al. [2] and Wang et al. [3] used axial scans

## Slide 5: Introduction – Tracked Ultrasound
Tracking info with images allow landmark location
Curvature extracted from landmarks

## Slide 6: Problem Description
Ultrasound methods do not rely on familiar visualizations
Shadow
Visible bone
Invisible bone

## Slide 7: Objective
Create surface visualizations of scoliotic spines from transverse process locations

## Slide 8: Contribution
A method for warping a healthy-shaped model to patients’ transverse processes

## Slide 9: Methods
Anchor point locations calculated from landmark locations
Anchor points offset towards anterior anatomy of vertebrae from landmarks

## Slide 10: Methods
Directions of offsets determined from local inter-landmark geometry
Cross product of axial and lateral vectors point in desired direction

## Slide 11: Methods
Landmark registration computes transforms which displace model points to patient points

## Slide 12: Methods
Thin-plate spline interpolates transforms, producing displacement field
Field is applied over model, warping it to patient anatomy

## Slide 13: Results
Average Hausdorff distance: 2.8mm
Maximum Hausdorff distance: 20.0mm
Ground-truth
Visualization

## Slide 14: Results
Average Hausdorff distance: 2.3mm
Maximum Hausdorff distance: 24.0mm
Ground-truth
Visualization

## Slide 15: Results
Average Hausdorff distance: 2.4mm
Maximum Hausdorff distance: 17.7mm
Ground-truth
Visualization

## Slide 16: Results
Average Hausdorff distance: 2.9mm
Maximum Hausdorff distance: 18.1mm
Ground-truth
Visualization

## Slide 17: Conclusions
Method produces informative visualizations
Validate with landmarks from ultrasound
Investigate robustness
1/2
1/3

## Slide 18: Thank you! Questions?

## Slide 19: References
Ungi T, King F, Kempston M, Keri Z, Lasso A, Mousavi P, Rudan J, Borschneck DP, Fichtinger G. “Spinal curvature measurement by tracked ultrasound snapshots”. Ultrasound in Medicine and Biology. 2014 Feb; 40(2):447-54.
Cheung CW, Zhou GQ, Law SY, Mak TM, Lai KL, Zheng YP. “Ultrasound Volume Projection Imaging for Assessment of Scoliosis”. IEEE Trans Med Imaging. 2015 Aug; 34(8):1760-8.
Wang Q, Li M, Lou EHM, Wong MS. “Reliability and Validity Study of Clinical Ultrasound Imaging on Lateral Curvature of Adolescent Idiopathic Scoliosis”. PLOS ONE. 2015 Aug; 10(8):1-16.