## Slide 1: Visualization of scoliotic spine using ultrasound-accessible skeletal landmarks
Ben Church1, Andras Lasso1, Christopher Schlenger2, Daniel P. Borschneck3, Parvin Mousavi4, Gabor Fichtinger1,3, Tamas Ungi1,3
Laboratory for Percutaneous Surgery, School of Computing, Queen’s University, Kingston, ON, Canada
Premier Chiropractic, Stockton, CA, USA
Department of Surgery, Queen’s University, Kingston, ON, Canada
Medical Informatics Laboratory, School of Computing, Queen’s University, Kingston, ON, Canada

## Slide 2: Introduction - Scoliosis
Scoliosis is lateral spinal curvature
Curvature often progresses until skeletal maturity
Regular assessment helps ensure early treatment

## Slide 3: Introduction - Assessment
Gold-standard assessment method is X-ray imaging
Cobb angle is measured
Quantifies severity of scoliosis

## Slide 4: Introduction – Tracked Ultrasound
Motivated by X-ray health risks
Methods typically locate skeletal landmarks
Curvature extracted from landmarks

## Slide 5: Problem Description
Current ultrasound methods do not produce easily interpreted visualizations

## Slide 6: Contribution
A method for producing informative spinal visualizations
Average shaped spine is warped to patient anatomy using registration points

## Slide 7: Contribution
We supplemented transverse process locations with anchor points to ensure registration is anatomically realistic

## Slide 8: Methods
Transverse processes located using patients’ prior CT scans
Anchor point locations calculated from landmark locations

## Slide 9: Methods
Anchor points offset towards anterior anatomy of vertebrae from landmarks
This conveys anterior-posterior scale and vertebral rotation

## Slide 10: Methods
Directions of offsets determined from local inter-landmark geometry
Cross product of axial and lateral vectors point in desired direction

## Slide 11: Methods
Landmark registration then computed the thin-plate spline deformation field which warps model points to the patients’
Deformation field was applied over average model, warping it to patient anatomy

## Slide 12: Methods
Results visualizations were assessed compared to ground truth CT scans
Model to patient distance maps and Hausdorff distances were computed

## Slide 13: Results
Average Hausdorff distance: 2.8mm
Maximum Hausdorff distance: 20.0mm

## Slide 14: Results
Average Hausdorff distance: 2.3mm
Maximum Hausdorff distance: 24.0mm

## Slide 15: Results
Average Hausdorff distance: 2.4mm
Maximum Hausdorff distance: 17.7mm

## Slide 16: Results
Average Hausdorff distance: 2.9mm
Maximum Hausdorff distance: 18.1mm

## Slide 17: Discussion
Visualizations convey overall form of patients’ spines
Misalignment mainly at superior and inferior ends, and in anterior anatomy

## Slide 18: Conclusions
Proposed method produces informative visualizations
Does not serve to replace quantitative measures, but to supplement them

## Slide 19: Ongoing Work
Investigating robustness with respect to missing, misplaced, or mislabeled landmarks
1/3
1/2
2/3
1/1

## Slide 20: Thank you! Questions?